| Relay | Stock No | Price (£) Each | Delivery |
| --- | --- | --- | --- |
| 12V Plain case | 4954787 | 1.20 | Ex-stock |
| 12V Plain case, diode | 4954923 | 1.53 | Ex-stock |
| 12V Bracket | 4954778 | 1.30 | Ex-stock |
| 24V Plain case | 4954784 | 1.35 | Ex-stock |
| 24V Plain case, diode | 4954926 | 1.59 | Ex-stock |
| 24V Bracket | 4954781 | 1.45 | Ex-stock |

# Text boxes

Features

- Dimensions & Characteristics according to ISO 7588

- Plug-in or bracket mount

Contact Data

Arrangement:			1 form C (1C/O) or 1 form A (1N/O)

Expected Life:			10 million operations, mechanical; 100,000 electrical

Rated Load:			40A 14VDC, resistive on N/O contact

Initial Breakdown Voltage:		500V rms, coil to contact

Contact Material:			AgSnO

N/O contact	N/C contact

Max make current (lamp load)	90A @ 16VDC	30A @16VDC

Max break current			40A @16VDC	30A @ 16VDC

Max continuous current:	@ 23°C	40A		30A

@ 85°C	35A		20A

Coil Data @ 23°C

| Nominal Voltage VDC | Operate Voltage (max) VDC | Release Voltage (min) VDC | Resistance ( ( 10% | Resistance with Resistor in Parallel ( ( 10% |
| --- | --- | --- | --- | --- |
| 12 | 7.8 | 1.2 | 90 | 79.5 |
| 24 | 15.6 | 2.4 | 360 | 317.5 |

New Low Cost Mini Automotive Relay

From Tyco

Cube/Mini Relays F

rom TYCO

Pennine Components Ltd

##### Distributors & Stockists of Electrical Components for Industry

PO Box 1, 65/67 Halifax Road, Todmorden, Lancs, OL14 5BB

Tel: 01706 815737	Fax: 01706 817628

##### E-Mail: sales@penninecomponents.co.uk

Web: 	  www.penninecomponents.co.uk

###### Visit our website @ www.penninecomponents.co.uk

Unit price 1 to 24 pieces, Consult for volume