- Electrically operated latching Battery Isolators.

- 300A continuous rating.

- Peak 1500A (5 Sec).

- IP65.

- M10 terminals.

- Kit includes protected Pushbutton and Buzzer (auto) and link harness.

- EEx ib II C T6  Ex II 2G.

- 100uA current consumption.

- Manual and Automatic models.

- Available in 24Vdc and 12Vdc.

# Text boxes

sales@penninecomponents.co.uk

www.penninecomponents.co.uk

PO Box No.1, 65/67 Halifax Road, Todmorden, Lancashire, OL14 5BB, England

Tel: 01706 815737	Fax: 01706 817628

Visit our website @ www.penninecomponents.co.uk

Visit our website @ www.penninecomponents.co.uk

DB3-24 Manual model. Vehicle power is connected or disconnected by pressing a single momentary pushbutton.

DB5-24 Automatic model. In addition to the pushbutton operation vehicle power is automatically disconnected 60 seconds after removing the ignition key. The buzzer will also sound if battery voltage is below 20Vdc or above 30Vdc.